## Slide 1
Chasing 365 µA
Debugging a XIAO ESP32-C6 deep sleep mystery
A pool-float power story — wrong theory, controlled bench, real answer
Scott Dube • Hands-On Tech / Small Computers
Notes: Open warm. Frame as a journey of being wrong then being right. ~10-15 min total + Q&A. Opening line idea: 'I want to walk you through a project where I followed a popular piece of internet wisdom down the wrong path, then dug myself out with a bench experiment. Pool float, ESP32-C6, deep sleep current.' Anchor on the three numbers: 15 / 89 / 333. If I get lost mid-talk, come back to these.

## Slide 2
The project
A battery-powered pool water-temperature sensor that has to survive 138 days unattended each summer
MCU
XIAO ESP32-C6 (low-power WiFi)
Sensor
NTC thermistor + 47 kΩ reference on GPIO1
Power
2× L91 lithium AA in series (3.0–3.4 V)
Cadence
Deep sleep, wake every 30 minutes, publish to HA
Antenna
U.FL external (case-internal)
Constraint
138 days unattended — sleep current matters
Insert: photo of the float in the pool
2 / 12
Pool float deep sleep debug
Notes: Context: float drifts in the pool while I'm in NH for the summer. Every microamp matters because cell capacity is finite. Optional aside if it lands: 'I built this because the OmniLogic in-pool temp probe reads unknown whenever the filter pump is off, which is most of the night. Independent sensor closes the gap.' Don't dwell on the specs — they're just the setup. Move to the symptom.

## Slide 3
The symptom
Deployed float was drawing way more current in deep sleep than it should
381 µA
OBSERVED
on the deployed modded float
~15 µA
TARGET
per the Seeed forum's BASIC example
Missing 365 µA. Where is it going?
3 / 12
Pool float deep sleep debug
Notes: Two big numbers, one question. Pause here. The amber 381 is what I measured on the deployed float. The teal 15 is what the Seeed forum's BASIC example says you can hit on a stock C6. Land the line: 'Where's the missing 365 µA going?' This is the hook for the rest of the talk.

## Slide 4
The theory I bought (yesterday)
Voltage trap below 3.5 V
A popular Seeed forum thread holds that the XIAO ESP32-C6's power management can't enter clean low-power sleep below ~3.5 V supply.
My L91 stack sits at 3.0–3.4 V across discharge.
Math close enough. Symptom matched. I wrote it into my notes and moved on.
Then a fresh C6 arrived and I decided to verify before locking it in for next-season hardware.
4 / 12
Pool float deep sleep debug
Notes: Walk through honestly. Don't be defensive about being wrong. The forum thread is real, the math nearly fit, the symptom matched. I bought it. The audience respects honesty — self-correction is the credibility move. The transition line at the bottom (Then a fresh C6 arrived...) sets up the bench work in the next slides.

## Slide 5
The bench setup
Fresh stock C6, PPK2 as both power source and current meter, one variable at a time
Nordic PPK2 in Source Meter mode at 3.300 V
Leads on the C6's 3V3 pin and GND
No USB, no battery, no modifications
Same supply topology as the deployed float
Add one piece at a time, watch the trace
Capture a sleep-only slice on each test
Insert: breadboard photo (C6 + 47 kΩ resistors + PPK2 leads)
5 / 12
Pool float deep sleep debug
Notes: This is the methodology slide. 'One variable per test' is the line to deliver — it's what makes the matrix possible. Fresh stock C6 means no modifications — exact same hardware anyone in the room could buy. PPK2 in Source Meter mode means it's BOTH the power source AND the current meter — sources 3.3 V and measures every microamp going in. Pause briefly on the photo so the audience can see the physical setup.

## Slide 6
What actually happened
Each row is one change from the row above. Sleep current measured in a flat 8–30 s selection between wakes.
Configuration | Sleep current
Stock C6, minimal firmware | 15.66 µA
Stock C6, full pool-float firmware (ADCs configured, nothing wired) | 15.66 µA
Add 47 kΩ + 47 kΩ NTC divider, high side on 3V3 | 333.77 µA
Move divider's high side to GPIO2 (LOW during sleep, gpio_hold_en) | 89.51 µA
Remove the second ADC sensor from firmware | 89.55 µA
Lift GPIO1 from the divider entirely (pin floating) | 89.53 µA
Change ADC attenuation 12 dB → 6 dB | 89.53 µA
Three numbers tell the story: 16, 89, 333.
6 / 12
Pool float deep sleep debug
Notes: THE HEART OF THE TALK. Slow down here. Walk down the table row by row: - Row 1 (15.66 µA): 'Stock C6, minimal firmware. This kills the voltage trap theory right here.' - Row 2 (15.66 µA): 'Same board, but now with the full pool float firmware loaded — ADC sensors configured, lambdas in place. Nothing wired up yet. Still 15. So the firmware alone isn't the problem.' - Row 3 (333.77 µA): 'Now I add just the resistor divider. The thing that reads the NTC temperature. Boom — 10x jump.' - Row 4 (89.51 µA): 'The fix — I'll explain in two slides. Recover 244 µA.' - Rows 5-7: 'I tried three more things to drop the last 74 µA. Nothing moved it. That tells me what's left is chip-level.'

## Slide 7
First surprise — there is no voltage trap
15.66 µA
fresh stock C6, 3.3 V on the 3V3 pin, exactly the supply voltage I was 'trapped' at
The Seeed forum's BASIC example reproduces fine.
The wrong theory is dead at row 1 of the matrix.
So where is my 365 µA going?
7 / 12
Pool float deep sleep debug
Notes: The 'voltage trap is dead' punchline. One big number on the slide. PAUSE. This is the moment the audience realizes the forum was wrong and that the matrix structure was the point of the methodology. Land the question at the bottom: 'So where is my 365 µA going?' That sets up the next two slides.

## Slide 8
Effect #1 — the divider costs 10× the math
Ohm's law predicts:
3.3 V ÷ 94 kΩ = 35 µA
Bench measured:
318 µA above the bare floor
Best read: the ADC pin's input frontend at 12 dB attenuation is loading the divider somehow — bias circuitry in the SAR ADC's analog frontend that the passive math doesn't capture.
Held loosely — I'm guessing at the mechanism, not measuring it.
Insert: PPK2 trace — 333.77 µA selection (divider on 3V3)
8 / 12
Pool float deep sleep debug
Notes: Show the math vs the measurement. The point: passive Ohm's-law math is off by 10x. Something else is going on. BE CAREFUL: I do NOT know the exact mechanism. My best read is something in the ADC pin's input frontend is loading the divider, but I haven't measured it directly. If a real EE in the room knows, I want to hear it. HOLD LOOSELY. This is one of two slides where I explicitly flag inference vs measurement. The audience will respect the distinction.

## Slide 9
Effect #2 — ADC subsystem bias, fixed cost
Four different tries to drop it. Same number every time.
Divider GPIO-gated
89.51 µA
GPIO0 ADC removed from FW
89.55 µA
GPIO1 lifted entirely (floating)
89.53 µA
Attenuation 12 dB → 6 dB
89.53 µA
My read (held loosely): ~74 µA chip-level bias just for having the ADC peripheral initialized.
Independent of channels, attenuation, or pin state.
9 / 12
Pool float deep sleep debug
Notes: The four 89 µA tests. Same number every time. Whatever this is, it's chip-level — independent of channels, attenuation, pin connections. My READ is that initializing the ADC peripheral in ESP-IDF keeps some reference circuit biased. Untested but plausible — adc_oneshot_del_unit() before sleep would test it. I didn't try. If anyone in the room wants to take that experiment, the setup is reproducible.

## Slide 10
The fix — one wire + 8 lines of firmware
Move the 47 kΩ reference resistor's high side from 3V3 → GPIO2. Drive HIGH on wake, LOW with gpio_hold_en before sleep.
on_boot priority-800 lambda
gpio_hold_dis((gpio_num_t)2);
gpio_reset_pin((gpio_num_t)2);
gpio_set_direction((gpio_num_t)2,
GPIO_MODE_OUTPUT);
gpio_set_level((gpio_num_t)2, 1);
before deep_sleep.enter
gpio_set_level((gpio_num_t)2, 0);
gpio_hold_en((gpio_num_t)2);
Insert: PPK2 trace — 89.51 µA selection (after GPIO-gating)
10 / 12
Pool float deep sleep debug
Notes: THE SLIDE I'LL FORGET BY NEXT FALL. Re-read the prep notes doc before presenting. A LAMBDA is a small block of C++ code dropped into the ESPHome YAML as an escape hatch. The word means 'small anonymous function' — chunk of code attached to an event ('when the device boots', 'before deep sleep') rather than to a name. The two lambdas: On WAKE (on_boot priority-800, runs VERY early in boot): - gpio_hold_dis = release the 'freeze' we put on GPIO2 before sleep - gpio_reset_pin = clear leftover config, fresh start - gpio_set_direction = tell the chip we're driving the pin (not reading) - gpio_set_level((gpio_num_t)2, 1) = pin HIGH (3.3 V), powers the divider so ADC can read Before SLEEP: - gpio_set_level((gpio_num_t)2, 0) = pin LOW (0 V), no voltage across divider, no current - gpio_hold_en = FREEZE the pin in LOW state so chip can't reset it during deep sleep The (gpio_num_t)2 syntax is a TYPE CAST required by the ESP-IDF API. Tells compiler 'treat the number 2 as a gpio_num_t identifier.' Pedantic but the API requires it. The whole point: GPIO2 acts like a SWITCH on top of the divider. Powered briefly during wake, dark for the rest of the time. Why GPIO2? On the ESP32-C6, pins 0-7 are 'RTC-capable' — they can be controlled by the always-on RTC subsystem (the part that stays powered during deep sleep). GPIO2 is in that range and was free. 20 mA default drive strength, divider draws 35 µA, 500x headroom. Don't read the code aloud. Highlight the pattern: HIGH on wake, LOW + hold on sleep.

## Slide 11
Runtime impact
Same L91 stack, same 30-minute cadence, single wire move + 8 lines of firmware.
BEFORE
287 days
381 µA sleep, deployed today
Clears 138-day window by 2×
AFTER (v2.1)
~668 days
89 µA sleep, GPIO-gated divider
2.3× more deployment runtime
Hypothetical full ADC deinit before sleep → ~1,000+ days. Untested. Next experiment if anyone wants it.
11 / 12
Pool float deep sleep debug
Notes: Before vs after. 287 days to 668 days. Reassuring framing: 'For context, my unattended window is 138 days. The original design clears that with margin. The fix doubles that margin.' Nothing was broken in deployment — the fix is a bonus, not a save. Floor note at the bottom: full ADC deinit could push runtime past 1000 days. Untested. Throw it as an open challenge to the audience.

## Slide 12
Takeaways
Forum wisdom needs verification.
The voltage-trap theory sounded right and the math nearly fit. It was still wrong.
Build a controlled matrix.
One variable per test. Three numbers (16, 89, 333) told the story cleanly.
The right tool matters.
PPK2 resolves sub-µA differences. A multimeter would have missed the 15-vs-89 distinction entirely.
Hold your conclusions loosely.
The facts (measurements) are solid. The explanations (ADC frontend bias) are inferred. Be honest about the difference.
Questions?
Notes: Land on takeaway #4 — facts solid, explanations inferred, honest about the difference. That's the methodology message the audience can reuse. Then 'Questions?' Anticipated Q&A (full list in the prep notes doc): - Why not DS18B20? Case reuse history. For new builds, yes. - Did you try adc_oneshot_del_unit()? Not yet. Obvious next experiment. - How sure are you about ADC frontend loading? Not very. Measurement is solid, explanation is inferred. - Did you try lower ADC attenuation? Yes, 6 dB vs 12 dB. Same 89 µA. - PPK2 cost? $179. Paid for itself in one afternoon of this debug. - Is deployed float fixed? No, running old design with 287-day projection. Fix lands at next maintenance pull. - Can I get the code? Yes, scottdube/lrd-ha-config on GitHub.